## Slide 1: Update on Design and CSR Simulation Study of Bunch Compressor for the PITZ THz SASE FEL Experiment
Anusorn Lueangaramwong, PITZ
DESY-TEMF winter meeting 28.11.2019

## Slide 2: Bunch Compressor Design at PITZ
Purpose
  To shorten saturation length in SASE FEL
  To propose a superradiant THz source & seeded FEL
Status of design
  Chicane angle = 19° (Minimum angle & No collisions in model)
  R56~-0.2 m
Dipole magnet optimized with shims
  Flat profile in bending axis
  Pole shoes will be modified in Zeuthen
bending axis
w/ shims
w/o shims
shims
Undulator
Gun&Booster
Note: Design is improved from H. Shaker et al., presented at FEL'19, 2019, paper TUP003.
CST EM studio--optimizer

## Slide 3: Study with Simulations
To check performance of the bunch compressor design
When considering
  CSR effect
  Space charge effect
  Use of B-field profile
  Charge ~ up to few nC
Simulations w/ & w/o CSR
  Scan charge up to 1 nC
  Scan longitudinal parameters
  Next: Import beam distributions from PITZ colleagues
D1
D2
D3
D4
Undulator
Gun&Booster

## Slide 4: Previous Study
Done by H. Shaker using CSRtrack
Old design (17-deg Chicane)
charge = 500 pC
Compression works
But we want to investigate more
with initial flat-top beam
with initial PITZ beam
H. Shaker et al., presented at FEL'19, 2019, paper TUP003.

## Slide 5: Simulation Programs
for CSR effect
Our Requirements
Fringe field (we import field profile from CST EM studio)
Space charge effect (we have low E beam ~ 16 MeV)
Programs (so far we know)
according to their manuals
program | track dim | csr | sp charge | import B field | fringe field
astra | 3d | no? | yes | 3d on "cavity" | w/ import file
impactt | 3d | yes | yes | 1d | Enge function
csrtrack | 3d | yes | no | no | no
xtrack | 3d | yes | yes (1d) | no | no

## Slide 6: IMPACT-t setup and disadvantage
fringe field
D1
D2
D3
D4
For fast scan
3D space charge
  x = bending axis
  Grid 64x32x64
  Time step = 1e-13 s
Fringe field
  extended to the maximum of 0.5m from dipole edge
  allow calculation of CSR in drift between dipoles

## Slide 7: Ideal Beam Input
For ImpactT and Elegant (benchmark)
Gaussian Beam
  500000 macroparticles
  p = 16 MeV/c
  geometric emittance = 1e-7m
  beta = 10 m, alpha = 0 (sigma x = 1 mm)
  sigma t = 3 ps
  sigma s = 0.9 mm
  dp_s_coupling = 0.9999
  sigma dp = 0.005, dp = p/p0
tail
head
Notes: Normalized emittance ~ 1um for <= 1nC
P = 17 MeV/c
  sigma t = 3-4 ps

## Slide 8: Beam size
ImpactT (default) results
ImpactT uses axes of ref. particle at each dipoles entrance and exit
Degradation of compression performance
  optimize longitudinal parameters?
  is overcompression a solution?
D1
D2
D3
D4
D1
D2
D3
D4
CSR on
CSR off
Space Charge effect is still on total dispersion ~ 0
Not compressing
mismatched slice transverse emittance due to CSR
charge = 1nC
charge = 1nC
Notes: Sigma x theoretically increases due to different CSR kicks along the longitudinal distribution in dispersive motions forming a mismatched slice transverse emittance

## Slide 9: Compression vs Bunch Charge
Evolution of filaments
1pC overcompressed
40pC
100pC
1nC

## Slide 10: Compression vs Bunch Charge (continue)
profiles
overcompressed
optimum
2 filaments
2 peaks
Charge > 100 pC
  forming 2 filaments or more
  larger bunch length
Charge ~1nc
  forming 2 peaks in profile

## Slide 11: 2-filament Beam @ 100 pC
Beam size
  Selected for longitudinal parameter scan
  Still compressing in last dipole
Still compressing
D1
D2
D3
D4
100pC

## Slide 12: Compression vs Coupling
for 100 pC
original value
t
p

## Slide 13: Compression vs Bunch Length
for 100 pC
original value
t
p
Overcompressed
Undercompressed

## Slide 14: Compression vs Total Energy Spread
for 100 pC
original value
t
p
Overcompressed
Undercompressed

## Slide 15: Benchmark with Elegant Results
No space charge and field profile
Beam size in x increases to 2.0 mm
compress bunch length only about 3.4 times
New shared Sirepo link for benchmarking with Elegant--> https://www.sirepo.com/elegant#/visualization/Qh52wQe0
1nC

## Slide 16: In Progress
use distributions from ASTRA tracking in Gun and Booster
100 pC, Initial
100 pC, Final

## Slide 17: Summary
Status
  Design of bunch compressor chicane (no collision with old elements)
  Dipole flat B-profile by CST studio optimizer
CSR study
  IMPACT-t is our first choice but we want to try others as well
  Charge scan : 2 filaments show up at around 100 pC, beam distortion at 1nC
  Longitudinal parameter scan : parameter “coupling” can optimize the beam compression