## Slide 1: Reduced Gun Simulations 1. Comparison 60MV/m Gun vs 50MV/m Gun, Flat Top Laser Pulse 2. Comparison for the worst case: Gun50+Gauss Laser Pulse 3. Summary and Outlook
Yauhen Kot
Summary for the S2E Meeting 28.10.2013

## Slide 2
Reduced Gun Simulations 1. Comparison Gun60 vs Gun50, Flat Top Laser Pulse 2. Comparison for the worst case: Gun50+Gauss Laser Pulse 3. Summary and Outlook

## Slide 3
XFEL Photo Injector Setup
settings used in the simulations
RF-Gun | Cathode Laser | Booster | ASTRA
Field Balance= 1.12 | Temporal Profile: Flat Top 2/20\2ps Gauss 10-14ps FWHM | ACC1: 8xTESLA cavities: 1st cavity centered at z=4.0401m  1st iris at z=3.637m | 200K particles
Ecath=50.00-60.00MV/m Phi=-1.9 deg | Transverse: radial homogeneous | Epeak=34.42MV/m Phase=6.31 deg | Rotational symmetry Mesh: NradxNlong=40x100
Solenoid: main centered at z=0.276m Bucking coil at compensation |  |  | Tuned Parameters: Main solenoid peak field Laser rms spot size Rms bunch length (?) Gun launch phase
Goals & Tasks: - minimized transverse emittance at the 1st quadrupole (z=14.44m) - matchable optics  b<60m, ¦a¦<4 @1st quadrupole |  |  | 

## Slide 4
Charge |  |  | 1nC | 
Max electric field in the gun, [MV/m] |  |  | 50 | 60
Laser form |  |  | FT 2/20\2 | 
WP | MaxB,[T] |  | 0.1894 | 0.2226
 | XYrms,[mm] |  | 0.580 | 0.440
eprs=14.44m, [mrad] |  |  | 1.035 | 0.709
esl,peaks=14.44m, [mrad] |  |  | 0.955 | 0.626
esl,avs=14.44m, [mrad] |  |  | 0.905 | 0.624
esl,mins=14.44m, [mrad] |  |  | 0.538 | 0.439
esl,maxs=14.44m, [mrad] |  |  | 1.030 | 0.704
dEsl,peak,rms [keV] |  |  | 2.555 | 1.238
Ip, [A] |  |  | 43.6 | 45.8
t rms, [mm] |  |  | 2.168 | 2.048
Beam optical functions after 1st accelerating module |  | b,[m] | 22.18 | 8.73
 |  | a | -3.99 | 0.030
+46.0 % projected emittance growth
+52.6% growth of emittance at the current peak
+45.0% average slice emittance growth
Operation with 1nC. Comparison Gun50 vs Gun60

## Slide 5
1nC at XFEL Injector with 50MeV and 60MeV Gun.
Emittance Comparison
 |  | Gun60 | Gun50
Working Point | MaxB, [T] | 0.2226 | 0.1894
 | XYrms,[mm] | 0.440 | 0.580
emittance | e,[m-6] | 0.7091 | 1.0120
rms bunch lenngth | t,[mm] | 2.048 | 2.094
Beam optical functions after the 1st accelerating module | b,[m] | 8.729 | 22.18
 | a | 0.030 | -3.99

## Slide 6
1nC at XFEL Injector with 50MV/m and 60MV/m Gun.
Emittance Stability
50MV/m Gun: stable emittance but more extreme beam optical functions

## Slide 7
1nC at XFEL Injector with 50MV/m and 60MV/m Gun.
Comparison of Beam Optical Functions

## Slide 8
Charge |  |  | 500pC | 
Max electric field in the gun, [MV/m] |  |  | 50 | 60
Laser form |  |  | FT 2/20\2 | 
WP | MaxB,[T] |  | 0.1892 | 0.2224
 | XYrms,[mm] |  | 0.360 | 0.285
eprs=14.44m, [mrad] |  |  | 0.544 | 0.439
esl,peaks=14.44m, [mrad] |  |  | 0.543 | 0.393
esl,avs=14.44m, [mrad] |  |  | 0.518 | 0.386
esl,mins=14.44m, [mrad] |  |  | 0.336 | 0.274
esl,maxs=14.44m, [mrad] |  |  | 0.572 | 0.426
dEsl,peak,rms [keV] |  |  | 1.209 | 0.735
Ip, [A] |  |  | 23.5 | 24.0
t rms, [mm] |  |  | 1.984 | 1.944
Beam optical functions after 1st accelerating module |  | b,[m] | 7.957 | 19.81
 |  | a | -1.113 | -0.605
Operation with 500pC. Comparison Gun50 vs Gun60
+23.9 % projected emittance growth
+38.2% growth of emittance at the current peak
+34.2% average slice emittance growth

## Slide 9
Charge |  |  | 250pC | 
Max electric field in the gun, [MV/m] |  |  | 50 | 60
Laser form |  |  | FT 2/20\2 | 
WP | MaxB,[T] |  | 0.1888 | 0.2220
 | XYrms,[mm] |  | 0.230 | 0.180
eprs=14.44m, [mrad] |  |  | 0.329 | 0.298
esl,peaks=14.44m, [mrad] |  |  | 0.325 | 0.252
esl,avs=14.44m, [mrad] |  |  | 0.308 | 0.246
esl,mins=14.44m, [mrad] |  |  | 0.212 | 0.175
esl,maxs=14.44m, [mrad] |  |  | 0.336 | 0.268
dEsl,peak,rms [keV] |  |  | 0.633 | 0.575
Ip, [A] |  |  | 12.31 | 12.47
t rms, [mm] |  |  | 1.880 | 1.884
Beam optical functions after 1st accelerating module |  | b,[m] | 12.77 | 42.13
 |  | a | -0.706 | -2.305
Operation with 250pC. Comparison Gun50 vs Gun60
+10.4% projected emittance growth
+29.0% growth of emittance at the current peak
+25.2% average slice emittance growth

## Slide 10
Operation with 100pC. Comparison Gun50 vs Gun60
With 1.4% growth of the projected emittance for Gun60 in order to get matchable beam optical functions
Charge |  |  | 100pC | 
Max electric field in the gun, [MV/m] |  |  | 50 | 60
Laser form |  |  | FT 2/20\2 | 
WP | MaxB,[T] |  | 0.1882 | 0.2218
 | XYrms,[mm] |  | 0.1228 | 0.133
eprs=14.44m, [mrad] |  |  | 0.1891 | 0.1945
esl,peaks=14.44m, [mrad] |  |  | 0.175 | 0.137
esl,avs=14.44m, [mrad] |  |  | 0.164 | 0.138
esl,mins=14.44m, [mrad] |  |  | 0.120 | 0.116
esl,maxs=14.44m, [mrad] |  |  | 0.177 | 0.143
dEsl,peak,rms [keV] |  |  | 0.473 | 0.367
Ip, [A] |  |  | 5.05 | 5.56
t rms, [mm] |  |  | 1.815 | 1.647
Beam optical functions after 1st accelerating module |  | b,[m] | 49.89 | 39.5
 |  | a | -2.568 | -2.013
-2.7% projected emittance growth
+27.7% growth of emittance at the current peak
+18.8% average slice emittance growth

## Slide 11
100pC at XFEL Injector with 50MeV and 60MeV Gun.
Emittance Comparison
Scan size: DMaxB x DXYrms=0.0025T x 0.080mm; Color range: 0.1891-0.3306 mm
 |  | Gun60 | Gun50
Working Point | MaxB, [T] | 0.2218 | 0.1882
 | XYrms,[mm] | 0.133 | 0.1228
emittance | e,[m-6] | 0.1945 | 0.1891
rms bunch lenngth | t,[mm] | 1.640 | 1.891
Beam optical functions after the 1st accelerating module | b,[m] | 39.5 | 49.89
 | a | -2.013 | -2.568

## Slide 12
100pC at XFEL Injector with 50MV/m and 60MV/m Gun.
Comparison of Beam Optical Functions

## Slide 13
Table: Change of some bunch parameters in % if the peak electric field of the gun is reduced from 60MV/m to 50MV/m. Laser Pulse profiles is Flat Top 2/20\2ps in both cases |  |  |  | 
Bunch Charge | 1nC | 500pC | 250pC | 100pC
Depr, [%] | 46.0 | 23.9 | 10.4 | -2.7
Desl,peak,[%] | 52.6 | 38.2 | 29.0 | 27.7
Desl,av, [%] | 45.0 | 34.2 | 25.2 | 18.8
D(dE)sl,peak, [%] | 106 | 64.5 | 10.1 | 18.9
Summary: Operation Gun60 vs Gun50
Flat Top Laser Pulse 2/20\2ps
Bunches with higher charge suffer more,
but the claimed design parameters may be hold

## Slide 14
Reduced Gun Simulations 1. Comparison Gun60 vs Gun50, Flat Top Laser Pulse 2. Comparison for the worst case: Gun50+Gauss Laser Pulse 3. Summary and Outlook
Worst case:
- Maximum peak electric field of the gun by 50MV/m
- Longitudinal laser pulse profile: gaussian with 14ps FWHM (rms 5.95ps)

## Slide 15
Operation with 1nC:
60MV/m Gun + FT 2/20\2ps vs 50MV/m Gun + Gauss 14ps FWHM
+112% projected emittance growth
+115% growth of emittance at the current peak
+67.8% average slice emittance growth
Different rms bunch length
Charge |  |  | 1nC | 
Max electric field in the gun, [MV/m] |  |  | 50 | 60
Laser form |  |  | Gauss 14ps FWHM | FT 2/20\2 ps
WP | MaxB,[T] |  | 0.1889 | 0.2226
 | XYrms,[mm] |  | 0.460 | 0.440
eprs=14.44m, [mrad] |  |  | 1.501 | 0.7091
esl,peaks=14.44m, [mrad] |  |  | 1.352 | 0.629
esl,avs=14.44m, [mrad] |  |  | 1.064 | 0.634
esl,mins=14.44m, [mrad] |  |  | 0.546 | 0.439
esl,maxs=14.44m, [mrad] |  |  | 1.38 | 0.704
dEsl,av,rms [keV] |  |  | 2.75 | 1.1
Ip, [A] |  |  | 41.3 | 45.8
t rms, [mm] |  |  | 2.384 | 2.048
Beam optical functions after 1st accelerating module |  | b,[m] | 19.64 | 8.729
 |  | a | -2.419 | 0.030

## Slide 16
Charge |  |  | 1nC | 
Max electric field in the gun, [MV/m] |  |  | 50 | 60
Laser form |  |  | Gauss 10ps FWHM | FT 2/20\2 ps
WP | MaxB,[T] |  | 0.1891 | 0.2226
 | XYrms,[mm] |  | 0.505 | 0.440
eprs=14.44m, [mrad] |  |  | 1.887 | 0.7091
esl,peaks=14.44m, [mrad] |  |  | 1.681 | 0.629
esl,avs=14.44m, [mrad] |  |  | 1.271 | 0.634
esl,mins=14.44m, [mrad] |  |  | 0.665 | 0.439
esl,maxs=14.44m, [mrad] |  |  | 1.698 | 0.704
dEsl,peak,rms [keV] |  |  | 3.36 | 1.1
Ip, [A] |  |  | 48.0 | 45.8
t rms, [mm] |  |  | 2.054 | 2.048
Beam optical functions after 1st accelerating module |  | b,[m] | 20.49 | 8.729
 |  | a | -2.535 | 0.030
Operation with 1nC:
60MV/m Gun + FT 2/20\2ps vs 50MV/m Gun + Gauss 10ps FWHM
+166% projected emittance growth
+167% growth of emittance at the current peak
+100% average slice emittance growth
Equal rms bunch length

## Slide 17
Operation with 250pC:
60MV/m Gun + FT 2/20\2ps vs 50MV/m Gun + Gauss 14ps FWHM
Charge |  |  | 250pC | 
Max electric field in the gun, [MV/m] |  |  | 50 | 60
Laser form |  |  | Gauss 14ps FWHM | FT 2/20\2 ps
WP | MaxB,[T] |  | 0.1884 | 0.2220
 | XYrms,[mm] |  | 0.2175 | 0.180
eprs=14.44m, [mrad] |  |  | 0.435 | 0.298
esl,peaks=14.44m, [mrad] |  |  | 0.430 | 0.252
esl,avs=14.44m, [mrad] |  |  | 0.353 | 0.246
esl,mins=14.44m, [mrad] |  |  | 0.201 | 0.175
esl,maxs=14.44m, [mrad] |  |  | 0.447 | 0.268
dEsl,peak,rms [keV] |  |  | 0.838 | 0.575
Ip, [A] |  |  | 12.56 | 12.47
t rms, [mm] |  |  | 1.972 | 1.884
Beam optical functions after 1st accelerating module |  | b,[m] | 21.45 | 42.13
 |  | a | -1.755 | -2.305
+46.0% projected emittance growth
+70.6% growth of emittance at the current peak
+43.5% average slice emittance growth

## Slide 18
Charge |  |  | 100pC | 
Max electric field in the gun, [MV/m] |  |  | 50 | 60
Laser form |  |  | Gauss 14ps FWHM | FT 2/20\2 ps
WP | MaxB,[T] |  | 0.1880 | 0.2218
 | XYrms,[mm] |  | 0.128 | 0.133
eprs=14.44m, [mrad] |  |  | 0.247 | 0.1945
esl,peaks=14.44m, [mrad] |  |  | 0.204 | 0.137
esl,avs=14.44m, [mrad] |  |  | 0.179 | 0.138
esl,mins=14.44m, [mrad] |  |  | 0.119 | 0.116
esl,maxs=14.44m, [mrad] |  |  | 0.219 | 0.143
dEsl,peak,rms [keV] |  |  | 0.476 | 0.367
Ip, [A] |  |  | 5.49 | 5.56
t rms, [mm] |  |  | 1.815 | 1.647
Beam optical functions after 1st accelerating module |  | b,[m] | 38.47 | 39.5
 |  | a | -2.425 | -2.013
Operation with 100pC:
60MV/m Gun + FT 2/20\2ps vs 50MV/m Gun + Gauss 14ps FWHM
+27% projected emittance growth
+48.9% growth of emittance at the current peak
+29.7% average slice emittance growth
Different rms bunch length

## Slide 19
Table: Change of some bunch parameters if the peak electric field of the gun is reduced from 60MV/m to 50MV/m and the Laser pulse profiles is changed from Flat Top 2/20\2ps to Gaussian. |  |  |  | 
Bunch Charge | 1nC |  | 250pC | 100pC
Laser Pulse Length FWHM, [ps] | 14 | 10 | 14 | 14
Depr, [%] | 112 | 166 | 46.0 | 27.0
Desl,peak,[%] | 115 | 167 | 70.6 | 48.9
Desl,av, [%] | 67.8 | 100 | 43.5 | 29.7
D(dE)sl,peak, [%] | 150 | 205 | 45.7 | 29.7
Dt rms, [%] | 16.4 | 0.3 | 4.7 | 10.2
Summary: Operation
Gun60 FT 2/20\2ps vs Gun50 Gaussian 14ps FWHM

## Slide 20
Reduced Gun Simulations 1. Comparison Gun60 vs Gun50, Flat Top Laser Pulse 2. Comparison for the worst case: Gun50+Gauss Laser Pulse 3. Summary and Outlook

## Slide 21
1. Comparison for 60MV/m Gun + FT 2/20\2 vs 50MV/m Gun + FT 2/20\2 done
 50MV/m Gun most probably fits the claimed design parameters of the beam
2. Comparison for 60MV/m Gun + FT 2/20\2 vs 50MV/m Gun + Gauss 14 ps FWHM
done for 1nC, 250pC and 100pC bunch charges
 severe emittance growth for the nominal design bunch charge of 1nC.
doesn’t fit any more in the claimed design parameters of the beam.
 different bunch length. Gaussian pulse must be shorter than 14ps FWHM
to produce the bunch of the same length as in the flat top case
Summary
Outlook
Finish comparison for the “worst case”: 500pC bunch charge,
equal bunch length at the exit
2. Implement the laser pulse form received from the laser group.