## Slide 1
The Machine Protection System
for the European XFEL
E. Castro on behalf of the MPS team
08.10.2013
Notes: How to edit the title slide
Upper area: Title of your talk, max. 2 rows of the defined size (55 pt)
Lower area (subtitle): Conference/meeting/workshop, location, date, your name and affiliation, max. 4 rows of the defined size (32 pt)
Change the partner logos or add others in the last row.

## Slide 2: Outline
Requirements of the MPS
MPS architecture and hardware
Operation
Schedule
Summary
Notes: Before you start editing the slides of your talk change to the Master Slide view:
Menu button “View” > Slide Master:
Edit the following items:
1. On the Title slide (second master slide)
a) Click to add title of your talk
b) Click to add subtitle (conference, location, name of the speaker, date)
2. On the Slide Master (first master slide)
a) The 1st row in the violet header: Delete the existent text and write the title of your talk into this text field b) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area.
Close Master View

## Slide 3: Requirements of the MPS
Protect the accelerator from damage produced by the electron or photon beam
Help to control the radioactive activation of the components
Facilitate the handling of the machine and minimize the downtime: veto sections in the accelerator and dynamic limitation of beam power
Failsafe behavior: able to cope with SEUs, power cuts, cable breaks, …
Fast reaction time to minimize the number of bunches that are lost after detection of an alarm and before an action is taken
The MPS should be highly reliable and “user-friendly”

## Slide 4: Requirements: Reaction times
Beam loss location | Distance from linac dump kicker | Min. number of lost bunches
Injector | –1970 m | 0
BC1 | –1810 m | 7
BC2 | –1610 m | 15
Linac center | –930 m | 44
Linac end | –320 m | 69
beam distribution | 40 m | 2
last undulator | 1040m | 44
LXFEL=3010 m (~10us)
FXFEL=4.5 MHz
Dumping beam in switchyard area would reduce the number of lost bunches inside SASE undulator sections:
Up to 100 bunches could be lost before laser is blocked

## Slide 5: MPS architecture
Issues: latency of electronics and signal transport speed  additional lost bunches
Solution:
  Distributed Master/Slave architecture: 2 Masters, 130 slaves
  MPS can act on injector laser or dump beam in case of beam losses
  Use of optical fibers: fast signal transmission, no EM interference
  Mixed daisy chain/star topology
  FPGA-driven logic
(XSE)
(XS1)

## Slide 6: MPS hardware
MPS uses µTCA technology: Telecommunication standard adopted by DESY.
  compact, versatile and cost-efficient option for ultra-high speed analog and digital signal processing
The Masters and Slaves are equipped with DAMC2 boards: MPS will profit from its extended use in XFEL
The RTM board feeds the alarm signals to the DAMC2.
45 in
7 out
MPS RS422 RTM
DAMC2
FPGA
4 I/O optical connections
µTCA in DESY: http://mtca.desy.de/index_eng.html
Dosi-Mon card

## Slide 7: Overall features
Scalability: system can grow
Every slave holds all information of all prior connected slaves
Slaves can hold one dosimetry board
Each input alarm/output action is recorded by DOOCS
Low latencies:
Interfaces:
  Master-Slaves communication via 4 serial in/out optical ports
  To Timing System via the µTCA backplane
  Signals from/to external systems via RS422 lines
MASTER
MASTER
MASTER
SLAVE
SLAVE
SLAVE
Alarms IN
Alarms OUT
82 ns
780 ns
1400 ns
Measurements done in August 2013.
An improvement in a factor 3 is expected
(plus 5ns/m)

## Slide 8: Operation: tasks
Collect the status signals and alarms from the output of subsystems in the accelerator
In case of alarms, evaluate the response using internal alarm-response matrices
Constantly inform the Timing System about maximum allowed bunches and available accelerator sections
In case of a critical situation, immediately stop the beam by directly acting on the laser or dump kicker
Forwarding certain signals to other subsystems (e.g. Cryo OK signal)

## Slide 9: Operation: data structures
The two Master boards collect the information about the status of the devices connected to the slaves and generate:
Beam Modes: amount of bunches allowed in accelerator sections
Section Patterns: beam permissions in several accelerator subsections
Beam Modes
Section Patterns

## Slide 10: Operation: interface with Timing System
Beam Modes and Section Pattern are forwarded to the Timing System
Together with the requested bunch patterns from the operator, the Timing System will generate the table of allowed Bunch Patterns for each macro-pulse (10Hz)
(Bunch pattern: 32 bits with info about bunch charge and path to follow in XFEL)
Interface between the MPS and Timing System
MPS and Timing System are asynchronous
MPS and Timing masters in the same crate
MPS and Timing slaves in diagnostics crates along XFEL
Communication allows time stamping

## Slide 11: Operation: systems connected to the MPS
The MPS receives ~2000 status signals from systems in the XFEL
It will react inmediately to alarms following a predefined reaction protocol:
Establishing a new injection scheme for next macro-pulse (slow reaction)
In case of dangerous operating conditions, shutting down laser or dumping beam directly within a macro-pulse (fast reaction)
System | Approximate number of signals from MPS | Speed of outgoing signals | Subsystems’ task
Dump kicker | 1 | Fast | Dump beam
Distribution kicker | 2 | Fast | Distribute beam to SASE lines
Laser (output) | 2 per laser | Fast | Laser pulses
System | Approximate number of signals to MPS | Speed of incoming alarms | Subsystems’ task
Vacuum | 30 | Slow (sec) | Determine Operation Mode
Cryo | 10 | Slow (sec) | Determine Operation Mode
Magnets bending I & BC sections (warm) | 5 | Slow (sec) | Determine Operation Mode
Magnets bending undulator sections (warm) | 5 | Slow (sec) | Lead beam to linac dumps
Magnet steerers & quads (cold & warm) | 600 | Slow (sec) | Steer and focus beam
Coupler interlock | 28 (+3 later) | Fast | RF protection
LLRF | 56 | Fast | Steering beam
Klystron interlock | 28 | Fast | RF for beam
Modulators | 28 | Fast | RF for beam
BLM | 350 | Fast | Monitor beam losses
BHM | 24 | Fast | Halo monitor
Wire scanner | 44 | Slow (sec) | Diagnostics
TPS | 32*6 | Fast | Monitor beam loss
BPM | 72 | Fast | Orbit position
Dump diagnostics | 30 | Fast | Protect dump and avoid radiation activation
Dump kicker | 1 | Fast | Dump beam
Distribution kicker | 1 | Fast | Distribute beam to SASE lines
Laser | 1 per laser | Fast | Laser pulses
OTR screens | 27 | Slow (sec) | Diagnostics
OTR screens in TDS | 8 | Slow (sec) | Diagnostics
Photon Beamlines | 9 | Slow | Protect photon beamline components
Collimators | 5 | Slow | Protection of Undulator sections
Beam OFF | 1 | fast | Switch all Beam OFF manually
Radiation monitors | 390 | Slow | Measure radiation
Personnel Interlock | 12 | Fast | Information
Timing System | 150 | Fast | Running information
MPS | 2000 | Fast | Alarm information
Systems connected to the MPS
MPS output signals

## Slide 12: Operation: interaction with XFEL subsystems
All of the persons responsible for the XFEL equipment have been contacted for the elaboration of the CDR. Following points were agreed:
Each subsystem will provide the alarm signal in RS422 standard
Minimum duration of the signal is 100ns
It should be possible to mask alarms to prevent unnecessary XFEL downtime:
  Internally by experts in the subsystems
  Externally from the MPS
Personnal Interlock and Manual Beam Off can bridge the MPS control and stop the beam if needed

## Slide 13: Operation: MPS alarm response
Taking into account the location of the alarm and the source, the MPS builds a possible reaction scheme.
Location of alarm | Injector | Accelerator |  |  |  |  |  | SASE 1/3 (Alster) | SASE 2 (Elbe)
 | I 1 | BC 0 | L 1 | BC 1 | L 2 | BC 2 | L 3 |  | 
MPS response | Stop Beam | STOP Beam until I1 mode |  |  | STOP Beam until BC1 mode |  | STOP Beam until BC2 mode | DUMP Beam for this section | DUMP Beam for this section
Example: vacuum alarm along XFEL
Location of alarm | Injector | Accelerator |  | TLD | T4D (Alster) | T5D (Elbe)
 | I1D/I2D | B1D | B2D |  |  | 
MPS response | Stop Beam or reduce number of bunches | Stop Beam or reduce number of bunches | Stop Beam or reduce number of bunches | Stop Beam or reduce number of bunches | Dump Beam for this SASE line | Dump Beam for this SASE line
Example: alarms in the dumps

## Slide 14: Operation: safety of beam transport and experiments
The equipment protection system of photon beam lines and experiments is integrated in the machine MPS:
Provides: signals from X-ray BLMs and desired Beam Mode
Safety highly dependent on the MPS Beam Mode
Challenge: to eventually decouple 15 experiments running in 5 SASE beamlines.
5 experiments, different
beam requirements but
operating with same e- beam

## Slide 15: Operation: Organigram of responsibilities
Each of the monitors connected to the MPS are responsible for the tuning of their operation conditions (number of bunches that can withstand, thresholds,…) and detect alarms properly.
Systems such as LLRF, photon beamlines are equipped with interlock systems to ensure the protection of equipment. The MPS receives their interlock signal.
The MPS is responsible of reacting to the alarms.

## Slide 16: Operation: MPS failsafe operation
The failsafe operation of the MPS system does not rely on hardware redundancies. The correct communication between masters and slaves is guaranteed by special algorithms built on counters, parity bit, detection of broken lines, …
However, critical connections (to laser controller or dump) can be set up redundantly.
A cable break or short circuit in RS422 lines will be detected and reported as a normal interlock signal without specifying the type.
Subsystems connected to MPS are responsible to provide a reliable signal.

## Slide 17: Operation: Configuration and visualization
Configuration:
Masters and slaves boards are configurable through JDDD displays connected to DOOCS MPS servers.
After a power cut or hardware-reset the static configuration (reaction to alarms) has to be uploaded from DOOCS into the FPGA
Visualization:
The status of the MPS will be displayed with JDDD GUIs, for experts and operators.
Alarm analysis and handling
Every MPS board has an alarm logging and a time stamp for every event.
The post-mortem analysis will be done using the alarm logging and time stamps provided by the subsystems.
The handling of alarms will be done automatically by the MPS, or manually by the operator.
Expert config panel JDDD
MPS-server DOOCS
MPS-board DAMC2
Dosi-Mon FMC-card
config-file
Operator panel
Expert operation panel JDDD
Server tasks:
Synchronize static configuration
Provide status signals to displays
Log events

## Slide 18: Operation: MPS configuration
MPS configuration panel for FLASH

## Slide 19: Operation: MPS visualization
Info per MPS-slave and master
State of diagnose inputs
State of digital outputs
Proposed Section Pattern and Beam Modes
Board events with time stamps
MPS expert view for FLASH

## Slide 20: Schedule
So far, the schedule of the MPS fits into the XFEL timetable
 | Hardware | Software
Design | MPS-RTM version 1 done and tested | Almost done
Manufacturing/ Implementation | 24 RTMs are ready for installation. Next generation will be produced starting December 2013 or January 2014 | Almost done
Installation | first boards installed for the XFEL gun test. Rest of installation will be done next year in parallel with Timing System. | 
Commissioning | will be done inmediately after a system is connected to the MPS | 

## Slide 21: Summary
The development of the MPS for the XFEL is ongoing as planned
Each of the suppliers of status signals to the MPS was contacted to clarify their integration into the final design of the system.
A rough plot of the reaction protocol of the MPS to the alarms was elaborated.
The first installation of the MPS for the XFEL injector was successfully done
We will gain operation experience at FLASH II before the startup of XFEL
More info in the MPS CDR (EDMS number D00000003387601)