## Slide 1: RF control and beam acceleration under XFEL conditions
Studies of XFEL-type Beam Acceleration at FLASH
Julien Branlard, Valeri Ayvazyan, Wojciech Cichalewski, Mariusz Grecki, Mathieu Omet, Sven Pfeiffer, Christian Schmidt, Nick Walker
DESY, 24.5.2015

## Slide 2: Talk Outline
Motivation for the study
  9mA study runs
  Shift studies at FLASH (RF settings XFEL ≠ FLASH)
Shift outcome
  Achievements from RUN1, RUN2, RUN3 and XFEL follow up study
  Data analysis
Conclusions
  Side effects (good and bad)
  Tradeoff
  Optimal QL ?

## Slide 3: A bit of history…
FLASH seminar:
“ILC 9mA tests at FLASH“
02.07.2012

## Slide 4: Short History of the “9mA run”, for the ILC
2007
  Pushing towards long bunch trains and high beam currents
2009
  9mA beam operation
  Near quench operation
  Beam loading induced gradient tilts
2011
  First attempt at compensating gradient tilts using QL
2012
  Ql studies
  Quench studies
  Power overhead studies
QL adjustment
longer bunch train

## Slide 5: John Carwardine’s slides: Check-list of TD Phase accomplishments
Long bunch trains, heavy beam loading demonstration
  6mA / 800us demonstrated ( TDR Baseline)
  9mA / 800us marginally achieved (luminosity upgrade)
Vector Sum control of RF unit
  Operation of RF units comprising 16 and 24 cavities
  Intra- and inter-pulse stability better than 0.02%
Operating gradients
  Operation up to average of 29MV/m (24MV/m to 33MV/m)
  Lorentz-force detuning compensation on all cavities simultaneously
Pk/Ql control for optimizing gradient profiles
  Demonstrated flat gradient solutions to +/-0.3%
  ILC baseline has more knobs (power ratios), so easier
Operation close to quench
  Operation of several cavities close to quench (5-10%) at 4.5mA, 800us
  Quench detection / prevention and rapid recovery after quench
John Carwardine
GDE PAC: May 2012

## Slide 6: “What’s QL and why is it 3e6 at FLASH and 4.6e6 at XFEL ?”
Controls the input power coupling to the cavity
Higher QL  smaller bandwidth
  QL = 3.0e6 BW = 433 Hz FLASH
  QL = 4.6e6 BW = 283 Hz XFEL
QL impacts:
  Power budget (cost)
  Sensitivity to microphonics (performance)
  Power overhead for FB controls (performance, cost)
How to choose QL ?
  Match for nominal beam at nominal gradient
Facility | IBEAM | QL | TFILL
FLASH | 9.0 mA | 3.0e6 | 500 us
XFEL | 4.5 mA* | 4.6e6 | 750 us
* IBEAM(nominal)= 1.35 mA

## Slide 7: “XFEL-like” studies at FLASH
Investigate the impact of setting QL = 4.6x106 instead of 3x106
  Impact on the cavity modes (i.e. 8/9, 7/9)
  Impact on the RF control stability (i.e. dA/A, dPhi)
  Impact on the multi-beamline control (FLASH1 / FLASH2)
  Impact on the power budget
What is the “best” QL to operate the XFEL ?
  Given the time constraints (modulator and klystron)
  Given the moderate beam loading (XFEL Inom. = 1.35 mA)
  Simulation vs. experiment
Notes: QL = 4,7e6 is matched conditions for 5 mA
Add motivation slide to explain the history of 4.6e6 in XFEL TDR… legitimate to ask if 4.6e6 still the optimal QL

## Slide 8: “XFEL-like” studies at FLASH
RUN1: 2015.07.02 (afternoon and night shifts)
  The goal of this study is to demonstrate the XFEL stability requirements (0.01 % in amplitude and 0.01 deg in phase), for XFEL nominal beam current (1–1.5 mA), and at an average accelerating gradient of 23.6 MV/m, using XFEL RF control parameters (QL = 4.6e6).
RUN2: 2015.11.16 (morning, afternoon and night shifts)
  In this phase we would like to continue the studies already performed in July of this year, with the final goal of demonstrating multibeam operation with long pulses. Furthermore we would like to explore the option of pushing the beam currents higher in order to see stronger beam loading.
RUN3: 2016.01.28 (morning, afternoon and night shifts)
  The goal of this study is to investigate in details the impact of changing QL and the fill time on the LLRF controller stability and the overall power budget. The impact of changing QL on the beam loading will also be investigated.

## Slide 9: “XFEL-like” studies at FLASH
LLRF setup
  LLRF setup (changing QL, changing timing, connecting piezos: tunnel access)
  Piezos: always need to bring back up system because not running routinely at FLASH
  Only showed that we would be able to run with piezo but actually didn’t take measurement WITH piezos
Machine setup
  High machine setup times (3 MHz x 5 Hz versus 1 MHz x 10 Hz)
  Complications due to shifting to 3MHz  we stayed with same machine/laser rep rate in the last run (we “gave up” high current)
Beam setup
  Transmission to 1 nC, problems above 1 nC
unchanged
BEAM
Notes: Piezos: always need to bring back up system because not running routinely at FLASH
Only showed that we would be able to run with piezo but actually didn’t take measurement WITH piezos
Complications due to shifting to 3MHz  we stay with same machine/laser rep rate in the last run (we “gave up” high current)

## Slide 10: Talk Outline
Motivation for the study
  9mA study runs
  Shift studies at FLASH (RF settings XFEL ≠ FLASH)
Shift outcome
  Achievements from RUN1, RUN2, RUN3 and XFEL follow up study
  Data analysis
Conclusions
  Side effects (good and bad)
  Tradeoff
  Optimal QL ?

## Slide 11: RUN1 achievements
Commissioning of the automatic QL adjustment software
Recommissioning of the piezo control and automation

## Slide 12: RUN1 achievements
Demonstration of XFEL stability requirements
  with XFEL RF parameters
  with low beam current
XFEL specs: dA/A = 0.01%
dPhi = 0.01deg
Amplitude of ACC67: 500 RF pulses (grey), average (blue)

## Slide 13: RUN1 achievements
Impact of changing QL on the single cavity modes
Note: ADC have been replaced since  many less spikes
Notes: Repeat measurement with new ADC boards

## Slide 14: RUN2 achievements
System identification with the new RF parameters (QL change)
QL = 3e6
QL = 4e6
Only minor system changes  MIMO controller adjustment is not necessary for ACC67
Depends on the RF system (location of passband modes in VS)
@10kHz: OVC changes A/P driving signal
@7/9 mode: spread of 7/9 modes for VS?
+0.3dB
-0.4dB
Matches theory for single cavity
8/9
7/9
expected and observed model changes
Notes:     @ 10kHz: higher Ql  larger fill-2-flat drop  different working point on the non-linear klystron curve

## Slide 15: RUN2 achievements
Full beam transmission though FLASH I (1200 bunches) and FLASH II (30 bunches), 0.4 nC on-crest
Impact of changing QL on FLASH I - FLASH II transients
XFEL specs: 50 usec transition time
Notes: Delta_t is the time the transient oscillations take to fall back within the XFEL specificiations (0,01%, 0.01deg) ON TOP of the allocated 50 usec ? Is this true ?

## Slide 16: RUN3 achievements and follow up at XFEL A1.I1
QL and fill time parameter study
For each data point, measure:
  controller performance with and without beam
  total power usage (i.e. fill time + flat top) in closed-loop operation
TFILL QL | 500 usec | 650 usec | 750 usec
2.0e6 |  |  | 
3.0e6 |  |  | 
4.0e6 |  |  | 
4.5e6 |  |  | 
4.6e6 |  |  | 
beam ON (1nC) & beam OFF
2 data sets
ideal (FF)
experimental (FB)

## Slide 17: RUN3 achievements and follow up at XFEL A1.I1
QL and fill time on power budget
ideal case
quadratic fit
No beam

## Slide 18: RUN3 achievements and follow up at XFEL A1.I1
QL and fill time on power budget (continued)
Power overhead is defined as the relative difference between the measured data and the idea value
increase with QL
increase with fill time
first data points of the day
No beam

## Slide 19: RUN3 achievements and follow up at XFEL A1.I1
QL and fill time on stability
dA/A
dPhi
0 nC
0.5 nC
1.0 nC
Stability degrades with charge
Stability degrades with QL

## Slide 20: RUN3 achievements and follow up at XFEL A1.I1
QL and fill time on stability (continued)
0 nC
0.5 nC
Colors only denote different measurement points

## Slide 21: Talk Outline
Motivation for the study
  9mA study runs
  Shift studies at FLASH (RF settings XFEL ≠ FLASH)
Shift outcome
  Achievements from RUN1, RUN2, RUN3 and XFEL follow up study
  Data analysis
Conclusions
  Side effects (good and bad)
  Tradeoff
  Optimal QL ?

## Slide 22: Side effects
C8.ACC7 field emission  dark current activation
  What caused it?
  What’s happening (follow-up shifts)?
Piezo recommissioning
LLRF system improvements
  BLC, LFF
  Optimal SP QL
“What is indeed the best QL ?”
  Refocus of the shift goals
Lessons learnt for the XFEL ?
Notes: No hard proof, suspicion that C8.ACC7 was triggered by Ql change
Christian will coach Julien about limitation s of current implementation of the BLC
Should LFF learn from truncated pulses, the root of the problem is BLC is not perfect

## Slide 23: Fill versus Flat-Top Forward Power (trade off)
tfill = 750 ms
tflat = 650 ms
Ib = 5 mA
Eacc = 23.6 MV/m
minimum average power at lower Qext
minimum flat-top power at “matched” Qext
( = Pbeam)
PFOR during fill time reduced

## Slide 24: Conclusions
There is nothing magic about 4.6e6
  The choice of 4.6e6 was based on full beam loading, valid for CW, but fails for pulse system, because one needs to take fill time take into account
  lower bandwidth  more sensitive to detuning & microphonics  also requires more power for FB control
Piezo operation will help!
We would be better off at lower QL
   better stability (larger bandwidth)
   reduced power overhead for controls (follows from above)
   reduced average forward power
   reduced power during fill (which tends to be the peak operationally)
   higher forward and reflected power during the flat-top
There is actually flexibility
  one could operate the machine at a different QL

## Slide 25: Thank you for your attention!
Photo: Dirk Noelle

## Slide 26: BACKUP SLIDES

## Slide 27: FLASH I – FLASH II transition
Courtesy: Valeri Ayvazyan: LLRF 2015, Shanghai

## Slide 28: Forward power waveforms
TFILL = 500 usec QL = 2.0e6

## Slide 29: Forward power waveforms
TFILL = 500 usec QL = 4.6e6

## Slide 30: Forward power waveforms
TFILL = 650 usec QL = 4.6e6

## Slide 31: Forward power waveforms
TFILL = 650 usec QL = 2.0e6