## Slide 1: Undulator linear taper. Wakefield energy loss measurement.
Sergey Tomin
DESY
DESY, September 24, 2024

## Slide 2: Undulator taper
Undulator tapering controls the resonance properties of the Free-Electron Laser (FEL) amplification process.
Linear taper:
SR + wakes
Nonlinear taper: SR + wakes + FEL
Resonance condition
Taper to compensate energy loss
Undulator parameter
At the moment it is manual 4D optimization.
Undulator length 225 m

## Slide 3: Undulator linear taper
Undulator tapering controls the resonance properties of the Free-Electron Laser (FEL) amplification process.
  Linear taper is defined by beam energy losses due to SR and wakefields in undulator vacuum chamber
  Spontaneous radiation is well know and can be easily calculated
Energy losses in SASE1/2 (35 cells) undulator due to wakefields and SR
Electron beam energy 14 GeV
SR losses are already taking into account by control system

## Slide 4: Undulator linear taper
Undulator tapering controls the resonance properties of the Free-Electron Laser (FEL) amplification process.
  Linear taper is defined by beam energy losses due to SR and wakefields in undulator vacuum chamber
  Spontaneous radiation is well know and can be easily calculated
  Wakefields energy loss calculation requires undulator wakefield function and current profile
    Analytical approximation of wakefield function was developed for EuXFEL undulator vacuum chamber by I.Zagorodnov
m, , mm, , m, m, mm,
I.Zagorodnov et al., Short-range longitudinal wake function of undulator lines at the European X-ray free electron laser, Nucl. Instrum. Methods A, vol. 1043, 2022, 167490
Analytical approximation
Wake potential
BPM
Pumping slot
Absorber

## Slide 5: Current profile reconstruction with CRISP - non invasive THz diagnostics
A direct measurement of the current profile in the time domain can be achieved using transverse deflecting structures (TDS) – invasive, beam losses, low reprate.
TDS
Screen

## Slide 6: Current profile reconstruction with CRISP - non invasive THz diagnostics
A direct measurement of the current profile in the time domain can be achieved using transverse deflecting structures (TDS) – invasive, beam losses, low reprate.
Coherent diffraction radiation is generated by the electron bunch passing through an aperture inside an aluminum screen
  The coherent radiation spectrum and current profile of the electron bunch are linked via Fourier transform
N. Lockmann et al, Non-invasive Longitudinal Profile Measurements of Electron Bunches Simultaneously to FEL Operation at MHz Rates, IBIC 2020
N. Lockmann et al, PRAB 23, 112801 (2020)

## Slide 7: Current profile reconstruction with CRISP - non invasive THz diagnostics
A direct measurement of the current profile in the time domain can be achieved using transverse deflecting structures (TDS) – invasive, beam losses, low reprate.
Coherent diffraction radiation is generated by the electron bunch passing through an aperture inside an aluminum screen
  The coherent radiation spectrum and current profile of the electron bunch are linked via Fourier transform
Assumed current profile:
Gaussian,
Rectangular …
Kramers-Kronig phase
computed modulus is replaced by measued . Or it is retained at those discrete frequencies where it agrees within the estimated experimental error margin.
Current profile can not be negative
Block diagram of the Gerchberg-Saxton algorithm
B. Schmidt et al, Benchmarking coherent radiation spectroscopy as a tool for high-resolution bunch shape reconstruction at free-electron lasers, PRAB 23, 062801 2020
Current reconstruction

## Slide 8
Problem:
  Beam energy monitors (BEM) is aimed for absolute energy measurement and they have low accuracy ~ 1%. Not enough to measure energy change of order of tens of MeV
Benchmark theory with experiment

## Slide 9: Benchmark theory with experiment
BEM #2 calibration with SR
Problem:
  Beam energy monitors (BEM) is aimed for absolute energy measurement and they have low accuracy ~ 1%. Not enough to measure energy change of order of tens of MeV
Solution
  Calibration BEM with spontaneous radiation – close undulators one by one
Obtained calibration factor for BEM#2

## Slide 10: Side story about SR based dispersion calibration
S.Tomin et al, First Measurement of Quantum Diffusion in the Undulator Radiation. FEL 2024, Warsaw.

## Slide 11: Benchmark theory with experiment
We scanned beam compression – beam current profile
Beam energy at BEM#1 kept constant with energy FB.
Current profile comes from CRISP reconstruction.
Measurements were relative. Assuming that in lowest compression the beam energy loss <0.5 MeV
We performed two scans with LH off and on. It means different maximum current at full compression.
Result of the experiment
Energy FB to keep BEM#1 readings constant

## Slide 12: Benchmark theory with experiment
We scanned beam compression – beam current profile
Beam energy at BEM#1 kept constant with energy FB.
Current profile comes from CRISP reconstruction.
Measurements were relative. Assuming that in lowest compression the beam energy loss <0.5 MeV
We performed two scans with LH off and on. It means different maximum current at full compression.
Result of the experiment
Energy FB to keep BEM#1 readings constant
low compression
full compression
over compression

## Slide 13: Benchmark theory with experiment
We scanned beam compression – beam current profile
Beam energy at BEM#1 kept constant with energy FB.
Current profile comes from CRISP reconstruction.
Measurements were relative. Assuming that in lowest compression the beam energy loss <0.5 MeV
We performed two scans with LH off and on. It means different maximum current at full compression.
Result of the experiment
Energy FB to keep BEM#1 readings constant
low compression
full compression
over compression
BCM readings

## Slide 14: Wakefield contributions
BEM#1
314m
40mm pipe

## Slide 15: Comparison with the linear taper scan tool. Shift 25.09.2023
SASE1 beam line
Beam Energy: 14000 MeV Photon Energy: 6300 eV
Measurement was done with E. Schneidmiller
Sign is “wrong” here

## Slide 16: Comparison with the linear taper scan tool. Shift 3.10.2023, I = ~8 kA
SASE2 beam line
Beam Energy: 14000 MeV Photon Energy: 6505.71 eV
Measurement was done with E. Schneidmiller

## Slide 17: Comparison with the linear taper scan tool. Shift 3.10.2023, I = ~5 kA

## Slide 18: Comparison with the linear taper scan tool. Shift 3.10.2023, I = ~3 kA

## Slide 19: Compare with SASE spectrum shift
Get radiation from 6-8 cells.
Find mean spectrum position on HIREX
Shift undulator (aka sliding window)
Measure mean spectrum position shift
Idea of M.Yurkov.

## Slide 20: Is CRISP good enough for current profile reconstruction?

## Slide 21: Is CRISP good enough for current profile reconstruction?
Beam head and tail cannot be distinguished due to the missing phase in CRISP signal
  Loss factor (mean energy loss) is the same for both cases
  Undulator taper compensates energy loss for lasing slice
Energy loss for center of mass: 75 and 53 keV/m.
For maximum current: 73 and 68 keV/m

## Slide 22: Is CRISP good enough for current profile reconstruction?
Beam head and tail cannot be distinguished due to the missing phase in CRISP signal
  Loss factor (mean energy loss) is the same for both cases
  Undulator taper compensates energy loss for lasing slice
CRISP reconstruction resolution is > 6fs
Noisy signal for low current
Energy loss for center of mass: 75 and 53 keV/m.
For maximum current: 73 and 68 keV/m

## Slide 23: Machine Learning?
Ocelot s2e accelerator model was developed
  tens of thousand simulations was performed with different RF parameters including physics effects: SC, CSR, wakes (40k particles).
  CRISP outputs was simulated from the beam current profiles
Ocelot accelerator model: 2nd order tracking, SC, CSR, wakes
Astra gun simulations
FFT
t [fs]
I [kA]
Beam current
FF
f [THz]
CRISP output

## Slide 24: NN for LPS prediction
NN network was trained:
  Input: CRISP form factor + RF parameters
  Output: LPS
Does this approach work better then CRISP reconstruction?
J. Kaiser, A. Eichler, S. Tomin, Z. Zhu, Machine Learning for Combined Scalar and Spectral Longitudinal Phase Space Reconstruction, IPAC23.

## Slide 25: Comparison of the CRISP, NN and ground truth
However if we need to compensate energy loss for particular slice we need to know current orientation. And here ML can help us

## Slide 26: Summary
We demonstrated the wakefunction is agreed with experiment
  It is essential to predict linear taper
  It can also improve FEL simulations
CRISP diagnostics can be used for non invasive current profile measurements and it can be trusted.
Machine learning
  It is useful already to improve the CRISP current profile reconstruction
  And ML can be potentially useful for LPS prediction  we started new ML project to predict LPS based on simulations + CRISP and other non-invasive diagnostics