## Slide 1: FLASH II.
The results from FLASH II tests
Sven Ackermann
FEL seminar
Hamburg, April 23th, 2013

## Slide 2: Motivation for FLASH II.
Generate more photon user beam time by fast switching
Variable gap undulators offer flexible, fast and easy way for wavelength changes largely independent from electron beam energy
Seeding for better photon beam quality

## Slide 3: The FLASH facility.

## Slide 4: The FLASH II Project.

## Slide 5: FLASH II – Parameters.
Electron beam | 
Beam energy | 450…1250 MeV
Norm. emittance | 1…3 mm mrad
Energy spread | 500 keV
Peak current | 2.5 kA
Bunch charge | 20 … 1000 pC
Bunch spacing | 1 … 25 µs 1 MHz … 40 kHz
Repetition rate | 10 Hz
Undulator | FLASH1 | FLASH2
Period | 27.3 mm | 31.4 mm
Segment length | 4.5 m | 2.5 m
Segments | 6 | 12 (14)
Gap | fixed 12mm | variable min. 9mm
Focusing | FODO | FODO
K-Parameter | 0.9 | <1.95

## Slide 6: FLASH II – Wavelength tunability.
Electron energy | Wavelength at FLASH1 | Wavelength at FLASH2
0.7 GeV | 12.9 nm | 10 … 40 nm
1.0 GeV | 6.5 nm | 6 … 20 nm
1.2 GeV | 4.1 nm | 4 … 13.5 nm

## Slide 7: FLASH II – Timing pattern (example).
500 µs
500 µs
50 µs
250 µs
98.2 ms
500 µs
RF fililing time
FLASH1
500 bunches
1 nC
High compress.
High energy
FLASH2
250 bunches
0.3 nC
Low compress.
Low energy
RF change time
RF emptying time
100 ms 10 Hz
No RF to modules
– Bunch charge FLASH1
– Bunch charge FLASH2
– RF signal (e.g. Amplitude)
– Kicker amplitude
Kicker rise
Kicker flattop
Kicker fall
t

## Slide 8: Summary of the tests.
LASER1 and LASER2 are both functional
  Different charges, repetition rates and bunch numbers could be generated
LLRF dual flat top tests have been successfull
  Both flat tops controllable
  Slow FB working (as long as bunch number stays the same)
  The LFF was only working for a single flat top.
  Using the second flat top the LFF had to be switched off, as it produces harmonics which wont be damped otherwise.
Optics mismatch between the end of ACC7 and „kicker“ have been studied
  Simulated gradient changes of 50 MeV in either direction did affect the SASE level by around 10% to 20%.
  Increase of losses in the collimator measureable, but acceptable.
Charge dependencies were investigated
  The needed changes in the RF parameters fit inside the transistion time window

## Slide 9: Test with two bunch trains (2013-01-13)
Adjust both UV injector lasers to the cathode
Get transmission with both lasers
Establish SASE
Change:
  Energy
  Compression
  Charge

## Slide 10: Starting with both beams centered on virtual cathode.
LASER 2
LASER 1

## Slide 11: Putting both bunch trains to same bunch charge.
30 bunches
20 bunches
50 µs gap

## Slide 12: Same lasing

## Slide 13: Different compressions are possible
Same charge!

## Slide 14: Different charges – different lasing

## Slide 15: Both bunch trains lasing on Ce:YAG
Both lasers on the cathode
LASER 1 only
LASER 2 only

## Slide 16: SASE-spectra of both bunch trains
Both lasers on the cathode
LASER 1 only
LASER 2 only
Spectrometer was not functional due to software reasons. Therefore only spectrometer camera images are shown

## Slide 17: Varying gradients of second flat top
Changed ACC1 and ACC39 for compression
Changed gradient in ACC4/5 for small photon wavelength changes (FLASH1 has fixed gap undulators)

## Slide 18: SASE-spectra of both bunch trains
Both lasers on the cathode
LASER 1 only
LASER 2 only
DEbeam ~ 7 MeV (1%)
Dl ~ 0.27 nm (2%)

## Slide 19: Test with two bunch trains – Lessons learned
  Produced two bunch trains with 30 and 20 bunches, each lasing
  Same charge, compression and energy led to same photon pulse energy
  Different bunch charges
  Different RF settings
  Lasers interchangeable
  Some tools work on a averaging basis, strange behaviour shown for the bunch pattern used (30 / 50 missing / 20).

## Slide 20: Simulation of mismatched optics (2012-04-14)
Match optics in linac
Change quads to match higher energies (+/- 50 MV)
Observe SASE

## Slide 21: Simulation of mismatched optics (2012-04-14)

## Slide 22: Measurements of injector optics

## Slide 23: SASE after matching

## Slide 24: Optics set for +0 MV - Transmission

## Slide 25: Optics set for +50 MV - Transmission

## Slide 26: Optics set for +50 MV - Optics

## Slide 27: More than 80% of SASE recovered

## Slide 28: Simulation of mismatched optics – Lessons learned
Mismatched optics for simulated energy deviations between -50 MeV and +50 MeV were studied.
Energy range was limited by the transverse collimator acceptance
Transmission and lasing were almost unaffected
Mismatched optics upstream the ECOL, for example for the different energies for FLASH1 and FLASH2 don‘t seem to be too problematic.

## Slide 29: Different charges (2012-04-13)
Establish SASE
Vary bunch charge
Measure bunch length
Measure SASE energy

## Slide 30: Charge – Bunchlength relation

## Slide 31: Charge – Bunchlength relation

## Slide 32: Charge – SASE energy dependence
Charge [pC] | SASE [µJ] @ 700 MeV | SASE [µJ] @ 1090 MeV
600 | 210 | 165/110*
300 | 170 | 80/100
150 | 110 | 75
70 | 30/55 | 35
RF station | Phase [°] | Amplitude | Transition time [µs]
GUN | - 8.0 | - 0.04 MW | 50*** for 5°
ACC1 | +/- 0.3 | +/- 0.7 | < 50**
ACC39 | +/- 1.0 | +/-0.6 | < 50**
ACC23 | +/- 3.0 | - 2.2 | < 50**
* Due to end of shift no further optimization was done
** Design performance for extraction kicker was switching time of 50 µs max.

## Slide 33: Further tests in 2013.
Explore larger energy and phase deviation ranges for the second flat top. This might be necessary for the seeding option of FLASH2.
A modified version of the LFF has to be tested
Charge dependency and bunch length test have to be repeated with both injector lasers
Tools have to be checked/modified for the dual flat top operation

## Slide 34: Thanks for your attention!
These FLASH II test were performed by
  S. Ackermann
  V. Ayvazyan
  B. Faatz
  K. Klose
  M. Scholz
  S. Schreiber