## Slide 1: FLASH RF gun developments.
Sven Pfeiffer for the LLRF team
FEL Seminar
Hamburg, 19.04.2016

## Slide 2: Outline
Introduction
LLRF
  Feedback & Limitations
  Learning Feedforward
Pulse Width Modulation
  RF gun cooling system
  Temperature estimation
  Precision temperature control
Fast Protection
  The why and wherefore
Current problems
  After start-up

## Slide 3: Outline
Introduction
LLRF
  Feedback & Limitations
  Learning Feedforward
Pulse Width Modulation
  RF gun cooling system
  Temperature estimation
  Precision temperature control
Fast Protection
  The why and wherefore
Current problems
  After start-up

## Slide 4: Introduction
(3) Protection:
Limiter for Output, FB, LFF etc.
Switch off the power to RF gun if necessary, e.g. spark
(2) Regulation - Water: Control the RF gun temperature  keep it on (slightly below) its resonance frequency
1.3 GHz SWS, Pulsed mode @ 10 Hz,
Forward power ≈ 5 MW (average power ≈ 50 kW)
Pulse length up to 800 μs  1% duty cycle
Since 01/2015 operated with MicroTCA.4
(1) Regulation - LLRF: Control the amplitude and phase of virtual probe signal

## Slide 5: Outline
Introduction
LLRF
  Feedback Loop
  Concepts & Achievement
Pulse Width Modulation
  RF gun cooling system
  Temperature estimation
  Precision temperature control
Fast Protection
  The why and wherefore
Current problems
  After start-up

## Slide 6: LLRF Regulation
Main.GUN Panel
LLRF
Ampl. SP [MV/m]
  (new: before power SP [MW])
Phase SP [deg]
Pulse length [μs]
Feedforward
Feedback
OVC, LFF etc.

## Slide 7: LLRF Regulation

## Slide 8: LLRF Regulation
System model
FPGA output to virtual probe
Model based optimization of
FB and LFF
Feedback loop
Small signal system model
Identified parameters:
I/Q gains as function of frequency
Cross-couplings
Bandwidth ~ 52 kHz
Loop delay ≈ 1.4 μs

## Slide 9: LLRF Regulation
1) Output-Vector Correction (OVC - Server)
  Drift compensation
2) Learning Feedforward (LFF - Server)
  Minimize repetitive errors from pulse to pulse
3) MIMO feedback (FB - FPGA)
  Intra-pulse feedback
Main limitation: Loop delay ≈ 1.4 μs
  limits control gain
    max. FB gain 2-3; SRF ≈ 20-40 (!)
Feedback concepts
Goal: dA/A<0.01%
d <0.01 deg (rms)

## Slide 10: LLRF Regulation
Goal: dA/A<0.01%
d <0.01 deg (rms)
PI feedback

## Slide 11: LLRF Regulation
PI feedback
0.01deg.
Factor 3-5 improvement necessary
Goal: dA/A<0.01%
d <0.01 deg (rms)
0.01%
9MHz  100kHz

## Slide 12: Outline
Introduction
LLRF
  Feedback & Limitations
  Learning Feedforward
Pulse Width Modulation
  RF gun cooling system
  Temperature estimation
  Precision temperature control
Fast Protection
  The why and wherefore
Current problems
  After start-up
Outlook

## Slide 13: RF gun cooling system
GUN Wasser
  Temperatur
  Wasserkreislauf
Cold water
Valves
RF gun
Warm water
Heater
Tank

## Slide 14: RF gun cooling system
  Long term error ± 1 bit (about 14mK rms)
  @Resolution (12 bit ADC)
  of 0.02 K – 0.03 K
Required stability for d < 0.01 deg
without LLRF control:
(

## Slide 15: RF gun cooling system
  Long term error ± 1 bit (about 14mK rms)
  @Resolution (12 bit ADC)
  of 0.02 K – 0.03 K
Required stability for d < 0.01 deg
without LLRF control:
(
TIRIS
+100mK
Pressure
+0.09bar
SASE
-35uJ

## Slide 16: Pulse Width Modulation
Idea: Usage of LLRF Signals
Needed is a high precision temperature estimation with no time delay for pulse to pulse feedback
Use pulse width modulation to control the dissipated power (heat balance) to the RF gun body within pre-defined limits

## Slide 17: Pulse Width Modulation
Idea: Usage of LLRF Signals
FLASH RF GUN data
Temp. sensor (12 bit ADC)
Delayed TIRIS (9s) and TIN (5s) information
  Transition from cavity body to sensor
  Low pass behavior of temp. sensor

## Slide 18: Pulse Width Modulation
RF GUN phase at 1st beam position (700μs) for 50 minutes
Without and with modulation to minimize disturbances from cooling water circuit Pulse to pulse compensation (10 Hz)
Improvement for phase x3 (dφ = 53 mdeg.  16 mdeg.)
RF GUN temperature stabilized by x5 (from 14 mK  3 mK)
Running @ FLASH, PITZ, (XFEL)
Blue: single pulse, Red: mean 100 pulses (10s@10Hz)
* Under review @ Physical Review Special Topics - Accelerators and Beams

## Slide 19: Pulse Width Modulation
0.01deg.
Goal: dA/A<0.01%
d <0.01 deg (rms)
0.01%
Remember:
Factor 3-5 improvement in phase is necessary using only LLRF control
Applying PWM:
No improvement of RF amplitude
  Detuning affects mainly the RF phase
Great improvement in standard deviation of RF phase
Achieved by using disturbance minimization of detuning with precision temperature control

## Slide 20: Pulse Width Modulation – Panel
PWM Feedback check box
Set-point (automatically computed)
Status indicator
Initialization (settings before PWM)
Manual (set-up, problem handling)
With Pulse Width Modulation
Start-up of RF gun  next slide
Without Pulse Width Modulation

## Slide 21: Additional Info
Using pulse width modulation – panel for start-up of RF gun
Direct response
RF gun is in resonance, to cold or to warm
Relative detuning / temperature information
What is the current optimal Iris set-point etc.
Δ Temperature
TIRIS and set-point
Flattop length

## Slide 22: Outline
Introduction
LLRF
  Feedback & Limitations
  Learning Feedforward
Pulse Width Modulation
  RF gun cooling system
  Temperature estimation
  Precision temperature control
Fast Protection
  The why and wherefore
Current problems
  After start-up

## Slide 23: Fast Protection
Implementation in FPGA (L. Butkowski, C. Schmidt et al.)
Threshold for reflected signal is defined (scaled by forward signal)
Cut RF pulse if reflected signal is too high (sparks, detuning, etc.)

## Slide 24: Fast Protection
6 Events since 01/2016  no known false alarms
Test of
concept
unknown
Water pressure
Water pressure
Reference phase jump
RF-6
timing (?)

## Slide 25: Outline
Introduction
LLRF
  Feedback & Limitations
  Learning Feedforward
Pulse Width Modulation
  RF gun cooling system
  Temperature estimation
  Precision temperature control
Fast Protection
  The why and wherefore
Current problems
  After start-up

## Slide 26: Current Problems
After RF gun start-up
  Phase at end is not on set-point
How to check?
  Look in LFF panel

## Slide 27: Current Problems
RF gun start-up without FB, LFF
  (1) Adjust OVC before FB and LFF is enabled
  (2) Enable FB, LFF
  FF correction are centered after a while
  FF correction limits: 7000 bits
   t = 0
  (3) FF correction tables 20 minutes later
  (4) After 40 minutes
  FF tables (Q channel) hits limit
     readback ≠ set-point
t = 0
t = 20 min
t = 40 min
Why?
  Slowly waveguide heating (guess)

## Slide 28: Current Problems
After RF gun start-up
  Phase at end is not on set-point
Why?
  Slowly waveguide heating (guess)
How to check?
  Look in LFF panel
What can I do?
  Adjust OVC phase by ~ -4 deg
t = 40 min
t = 40+x min

## Slide 29: Current Problems
After RF gun start-up
  Phase at end is not on set-point
Why?
  Slowly waveguide heating (guess)
How to check?
  Look in LFF panel
What can I do?
  Adjust OVC phase by ~ -4 deg
Why is it not done automatically?
  Most of the time OVC is OFF…
  OVC ON does not mean that its active…
  Active limiter deactivate OVC
t = 40 min
t = 40+x min

## Slide 30: Outline
Introduction
LLRF
  Feedback & Limitations
  Learning Feedforward
Pulse Width Modulation
  RF gun cooling system
  Temperature estimation
  Precision temperature control
Fast Protection
  The why and wherefore
Current problems
  After start-up
Thank you for your attention!