## Slide 1: Microbunching Instability: causes, consequences and control
Giovanni Perosa
EuXFEL, FPH group
Beam Dynamics Seminar Meeting
Hamburg, June 24th 2025

## Slide 2: Outline
PART 1: Introduction
  Start-up & build-up
  Impact of MBI
PART 2: Modeling
  Analytical description
PART 3: Control of MBI
PART 4: Simulations
  Particle tracking

## Slide 3
Disclaimer
The topics, papers, and results presented here are selected based on my «extensive»—albeit not exhaustive—experience with the subject. In my view, they represent a core set of significant contributions to the understanding of microbunching instability in LINACs.
Intrabeam Scattering (IBS) is mentioned as a teaser and NOT discussed in this seminar
A quite exhaustive discussion can be found at: 10.1103/PhysRevAccelBeams.28.044401

## Slide 4
PART 1: Introduction

## Slide 5
density mod.
energy mod.
LSC
acceleration
dispersive region
R56, CSR
z
Magnetic Bunch Length Compression
Beam Energy
LSC = Longitudinal Space Charge
CSR =
Coherent
Synchrotron
Radiation
= Lorentz factor
Start up & build up
Disomogeneity at wavelength ~1 𝜇m to hundreds of 𝜇m

## Slide 6
z
density mod.
energy mod.
LSC
acceleration
dispersive region
R56, CSR
Increased Energy Spread
Spurious harmonic content
Broadening
Freq. mixing
G. Perosa et al., PRAB 23 (2020)
S. Di Mitri & S. Spampinati, PRL 112 (2014)
Simulated 30 𝜇m wavelength, 1% amplitude at 100 MeV
Consequences
Disomogeneity at wavelength ~1 𝜇m to hundreds of 𝜇m

## Slide 7
Consequences on FEL
 1–few m modulations contribute to pedestal and generate sidebands.
<< 1 m modulations bring sidebands far from central peak, but can interfere with seeding laser, and generate large slice energy spread.
>> 1 m modulations bring sidebands within the intrinsic FEL bw, generally not harmful.
mod  4 m
G. Perosa et al., PRAB 23 (2020)
G. Marcus et al., PRAB 22 (2019)
SASE, Self-seeding or externally seeded FELs are all affected

## Slide 8
Consequences on Energy Spread
S. Spampinati et al., PRSTAB 17 (2014)
No MBI
With MBI
Parameters | Values
Charge | 500 pC
Energy spread | 2.0 (With MBI) MeV 1.2 (No MBI) MeV
Peak current | 400 A (C = 7)
Beam Energy | 1.21 GeV
Parameters | Values
Charge | 180 pC
Energy spread | 2.1 (With MBI) MeV 1.2 (No MBI) MeV
Peak current | 1000 A
Beam Energy | 4.3 GeV
With MBI
No MBI
J. Qiang et al., PRAB 20 (2017)

## Slide 9
Take-home message on MBI
Accumualtion of modulations in longitudinal phase space in a wide range of wavelengths , ~1 𝜇m to hundreds of 𝜇m
Cascade effect enhanced by LSC and CSR
It affects the FEL performances directly and indirectly
It affects the energy spread adding a correlated term

## Slide 10
PART 2: Modeling

## Slide 11
A bit of History
Both models aim at the description of a bunching factor considered as the harmonic content of the current profile
All models aim at the determination of a gain curve, which in the linear regime is the ratio of final and initial bunching
Time-independent, ultrarelativistic and with an average 𝜷-function
After the first measurement in 2001 and the conceptualization of SSY (2002), 2 main models were developed
Huang-Kim (HK)
Bosch-Kleman-Wu (BKW)

## Slide 12
HK: the standard approach
Starting from Poissonian shot noise
ChatGPT says: The Huang and Kim model is a linearized Vlasov-based analytical framework that describes the evolution and amplification of small initial density modulations in an electron beam due to collective effects such as longitudinal space charge and coherent synchrotron radiation.
Energy modulation induced by bunching are described via LSC impedance:
The kernel K is determined by the CSR impedance
Updating density and energy modulations

## Slide 13
BKW: the agile model
R56, CSR
LSC
R56, CSR
LSC
R56, CSR
LSC
R56, CSR
G. Perosa S. Di Mitri, Sci Rep 11 (2021)
to a matrix
Density modulation gain
Energy modulation gain
Each single matrix describes the action of an element on the 2D longitudinal phase space: impedances, dispersive sections etc
The beamline is therefore a product of matrices

## Slide 14
Semi-analytical approach
Uncorrelated effective energy spread is used as a figure of merit to benchmark the validity of the results
It also returns the modulations in the 2D longitudinal phase space
It determines the gain curve for a given beamline
where
Compressed initial energy spread:
IBS_induced energy spread:
Energy spread due to MBI:
Examples of slice energy spread: measurement vs model
S. Di Mitri et al., PRAB 28 (2025)

## Slide 15
Semi-analytical approach
Uncorrelated effective energy spread is used as a figure of merit to benchmark the validity of the results
It also returns the modulations in the 2D longitudinal phase space
It determines the gain curve for a given beamline
where
Compressed initial energy spread:
IBS_induced energy spread:
Energy spread due to MBI:
Examples of slice energy spread: measurement vs model
S. Di Mitri et al., PRAB 28 (2025)

## Slide 16
HK vs BKW: what do they agree on?
amplification
damping
Gain is proportional to the current I and to the energy modulations
Gain is peaked around
Gain is exponentially suppressed at short wavelengths by the uncorrelated energy spread: (Longitudinal) Landau Damping
S. Di Mitri et al., PRAB 28 (2025)

## Slide 17
HK vs BKW: what do they agree on?
w/ IBS
288 keV
+CSR, CER
290 keV
+ LH
349 keV
w/ IBS
288 keV
+CSR
289 keV
+ LH
395 keV
BK
HK
Agreement (within 20%) of BK and HK, both in gain and energy spread, 1- and 2-stage
Courtesy of S. Di Mitri

## Slide 18
Take-home message on MBI models
Aiming at the prediction of bunching factor and gain function
Based on «linear approximation»
HK and BKW are in good agreement, but BKW model is more flexible
Gain is strongly affected by the uncorrelated energy spread
HK
Integral linearized Vlasov eq., solved by iteration at 2nd order in kernel.
4 dipoles chicanes
LSC + CSR
BK
Matrix model for modulations in the 2D long. ph. sp.
Generic dispersive term
LSC+CSR+CER
VS

## Slide 19
Honorable mention: Vlasov solvers
Venturini’s works
Tsai’s works
Amstutz & Vogt’s SelaV₁D

## Slide 20
PART 3: Control

## Slide 21
Controlling MBI: Laser Heater
Laser Heater
Laser
Undulator
  To induce uncorrelated energy spread, for suppression of MBI via energy Landau Damping
  Laser Heater is a composed of a laser and a short undulator embedded in a 4-dipole chicane:
  UV laser-electrons collinear superposition
  Smearing of the laser-induced modulations in the second half of the chicane
  What is it?
  Why?

## Slide 22
Controlling MBI: Laser Heater
Laser Heater
Laser
Undulator
  To induce uncorrelated energy spread, for suppression of MBI via energy Landau Damping
  Laser Heater is a composed of a laser and a short undulator embedded in a 4-dipole chicane:
  UV laser-electrons collinear superposition
  Smearing of the laser-induced modulations in the second half of the chicane
  Why?
G. Perosa Simone Di Mitri, Sci Rep 11 (2021)
Parameters | Values
Charge | 650 pC
Peak current | 600 A (C = 11)
Beam Energy | 0.89 GeV

## Slide 23
Controlling MBI: Laser Heater
The damping depends on the matching condition between the beam size and the laser size
Gain function after BC1 and after BC2
Energy distribution after LH
Z. Huang et al. PRAB 7, (2004)

## Slide 24
Controlling MBI: Laser Heater (Does it actually work?)
LCLS
FERMI
PAL-XFEL
EuXFEL
SwissFEL
FLASH

## Slide 25
Controlling MBI: Laser Heater (Does it actually work?)
G. Marcus et al., PRAB 22 (2019)
Experimental evidence of the impact of LH on:
FEL pedestal
bunching factor
Fourier transform of the projected XTCAV images
Ratner et al., PRAB 18 (2015)

## Slide 26
Controlling MBI: Laser Heater (Does it actually work?)
S. Spampinati et al., PRSTAB 17 (2014)
Slice energy spread as a function of the energy spread added by the LH
There exists a compromise (and an optimal setup) to minimize the slice energy spread and reduce MBI

## Slide 27
Controlling MBI: Phase Mixing
Di Mitri, Spampinati, PRL (2014)
  Advantageous because is not increasing the uncorrelated energy spread of the beam
Use of BC2/transfer line R56 to mix the modulations
Integrated OTR intensity
Simulation of the «rotation» in LPS

## Slide 28
Controlling MBI: Transverse Landau Damping
A. Brynes et al., PRAB 27 (2024)
Dispersive motion coupled to betatron emittance: Hxx
  Advantageous because is not increasing the uncorrelated energy spread of the beam
  Less sidebands
  Less jitter

## Slide 29
PART 4: Simulations

## Slide 30
Another bit of History
Pioneering work based on ELEGANT (see also references therein)
Simulations of LSC+CSR
60 milions particles + low-pass filter + interpolation
NAFF (Numerical Analysis of Fundamental Frequencies) instead of FFT
Noise vs # of macroparticles
MBI comes from noise, therefore

## Slide 31
Parameters | Values
Charge | 180 pC
Energy spread | 2.1 (With MBI) MeV 1.2 (No MBI) MeV
Peak current | 1000 A
Beam Energy | 4.3 GeV
Start-to-end simulations
of MBI at LCLS with IMPACT
Particle tracking
J. Qiang et al., PRAB 20 (2017)
No MBI
With MBI
Left panels: Measurements
Right panels: Simulations

## Slide 32
Thank you for the attention

## Slide 33
Back-up Slides

## Slide 34
PART 5: Measurement

## Slide 35
Direct methods
Ratner et al., PRAB 18 (2015)
XTCAV
Laser Heater
BC1
BC2

## Slide 36
Courtesy of M. Veronese and C. Spezzani
The scheme uses a CaF2 prism to disperse the broadband CTR (Coherent Transition Radiation) radiation emitted by a metallic foil.
PbSe and Pyroelectric detectors are used to cover a wavelength range from 0.25 to 10 𝜇m, both translated across the radiation beam and spectra.
SPIR: SPectrometer in the InfraRed
Direct methods: SPIR
Based on

## Slide 37
Collection of MBI spectra as a function of the electron beam current
t ~20 ps
Laser Heater, standard configuration:
the whole beam experience
an “homogeneous” heating
In the standard configuration, MBI is exponentially suppressed when the induced energy spread is increased.
Direct methods: SPIR

## Slide 38
Artificial MBI
Collection of spectra from superimposed energy modulations in the beam as a function of the electron beam current
Laser Heater, beating technique:
the whole beam experience a modulation
at the beating frequency of laser pulses
t ~10 ps

## Slide 39
Direct methods
2D FFT transform
Radon transform

## Slide 40
Figures of merit

## Slide 41
z
density mod.
energy mod.
LSC
acceleration
dispersive region
R56, CSR
wavelength, ~1 𝜇m to hundreds of 𝜇m
HK vs BKW: what do they agree on?
Bunching factor:
1-D, shot noise
Energy modulation:
energy-dependent, s-integral
Final bunching factor:
HK
Integral linearized Vlasov eq., solved by iteration at 2nd order in kernel.
4 dipoles chicanes
BK
Matrix model for modulations in the 2D long. ph. sp.
Generic dispersive term

## Slide 42
FFT vs NAFF