########################################################################
#                                                                      #
#                                                                      #
#                              HERACLES                                #
#                            VERSION  4.6                              #
#                                                                      #
#                          30. January 1996                            #
#                                                                      #
#   Date of last change: 27.11.96, VERSION 4.6                         #
#   Changes by H. Spiesberger                                          #
########################################################################

++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

Changes in version 4.6 are described below

++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

Changes in version 4.5 are described below

++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

Version 4.4 of HERACLES has a new implementation of parton distribution
functions and options for several new parametrizations of the low Q2
behaviour of structure functions. A bug in the F_L implementation of
version 4.3 has been removed and additional options for the calculation
of alpha_s are provided.
The code word 'PARTON-DIS' has been removed and replaced by the
new one 'STRUCTFUN'. In addition, for the inclusion of F_L, the code
words 'FLONG' and 'ALFAS' are needed. Their use is explained below.

The following subroutines and functions have been changed or are new.
Details of the changes in the main program are listed at the end of 
this text.

Changed and new routines:
     Main program HSMAIN,
     HSBLKD (Block data), HSPRLG;
     HSPVER, HSLUFL, ULALPS, PYSTFU, PYSTPR;
     HSWPDF, HSSTRF, HSSTR1, HSSTAL, HSSTBK, HSF2BK, SIGVMES, VMESNUC,
     HSBKIN, HSSTDL, HSF2DL.

The following two routines have been removed:
     STRFALLM, TUNG.


OPTIONS FOR PARTON DISTRIBUTION OR STRUCTURE FUNCTIONS
------------------------------------------------------

The code word 'PARTON-DIS' has been removed. Instead, the new code word

    'STRUCTFUNC'

with the input data

     ISTRFC

is used to choose a parametrization of the structure functions input.
ISTRFC is constructed in the following way:

     ISTRFC = ILQMOD*100000 + ILIB*10000 + ICODE

where

     ILIB = 1 to choose parton distribution functions from PYSTFU.
              The subroutine PYSTFU has been taken from LEPTO 6.1
              and modified for the use in HERACLES.

          = 2 to use PDFLIB (H. Plothow-Besch). Calls are performed via
              PYSTFU, but the corresponding line has to be enabled and
              the library to be provided by the user.

          = 3 to use PAKPDF (K. Charchula). Calls are performed via
              PYSTFU. The user has to provide the library PAKPDF.
              Make sure that the data initialization of PAKPDF is done
              correctly.

     ICODE = VALUE(1), the identification code for the parametrization
              of parton distribution functions for PDFLIB ('MODE').

           = IPAR*100 + ISET, the identification code for use of the
              library PAKPDF.

     ILQMOD = 0 use unmodified parton distribution functions for all Q2.

            = 1 apply exponential low Q2 suppression factor to parton
                distribution functions.

            = 2 for low Q2 (for Q2 < 6 GeV^2) use F_1 and F_2 parametri-
                zations from Brasse (for W < 2 GeV) and Stein (for W >
                2 GeV). At large Q2, parton distribution functions
                defined by ICODE are used.

            = 3 for Q2 < 6 GeV^2 use parametrizations from Abramowicz,
                Levy, Levin, and Maor (for W > 2 GeV) together with
                Brasse (for W < 2 GeV).
                If ICODE = 0, the ALLM parametrization is used for high
                              Q2 as well,
                if ICODE .NE. 0, for large Q2 the parton distributions
                              as requested by ICODE are combined with
                              the ALLM parametrization.

            = 4 For x < 0.1 and \nu > 10 GeV, the parametrization by
                Badelek and Kwiecinski is used. For \nu < 10 GeV,
                x < 0.1, the Brasse and Stein parametrization is used.
                At larger x, the parton distribution functions from
                MRS, set D-' have to be used
---->           NOTE: other combinations of BK with PDF's are
                      inconsistent !
                It is recommended to use ILQMOD = 4 together with
                ICODE = 0, in which case the MRS D-' set is
                automatically chosen.

            = 5 The Donnachie - Landshoff parametrization for Q2 < 10
                GeV^2 together with parton distribution functions are
                used.
                If ICODE = 0, the set MRS B235 is chosen, since this
                gives the smallest discontinuities of the cross section.

The default values are ILQMOD = 1 (exponential low Q2 suppression)
                         ILIB = 1 (PDF's from PYSTFU)
                        ICODE = 7 (Morfin Tung set 3)


LONGITUDINAL STRUCTURE FUNCTION
-------------------------------

In version 4.4 also F_L is included when input for the code-word

                         'FLONG'

is specified. The input to read after code-word FLONG is IFLOPT.
The definition of IFLOPT coincides with the definition of LST(11) of
LEPTO 6.1:
            IFLOPT = LQCD + LTM*10 + LHT*100
and LQCD, LTM and LHT specifies whether QCD contributions, target mass
effects and higher twist should be included. See the manual of LEPTO
6.1 for details. HERACLES calls modified routines from LEPTO 6.1 to
calculate F_L either event-by-event (time-consuming) or by using a grid
and linear interpolation.

For the calculation of radiative corrections, F_L is needed for small
Q2, also in the limit Q2 -> 0. The prescription for F_L(Q2->0) is
determined by ILQMOD:
    ILQMOD = 2: The Brasse and Stein parametrizations with R = 0.18
                is used to calculate F_L.
           = 3: F_L is calculated by the ALLM parametrization.
    otherwise:  F_L is calculated from the order alpha_s result of
                perturbative QCD. For Q2 values smaller than Q2_0 =
                6 GeV^2, F_L is assumed to be independent of Q2 and its
                value is given by F_L(Q2 = Q20).

The default value is IFLOPT = 0

The new code word

                          'ALFAS'

with input data

        MST111, MST115, PAR111, PAR112

is used to provide information needed for the calculation of alpha_s
Alpha_s enters the calculation of F_L and is evaluated in the function
routine ULALPS. The routine ULALPS has been taken from JETSET 7.3 and
modified for the use in HERACLES.
The meaning of the input data corresponds to the parameters MSTU(111),
MSTU(115), PARU(111), PARU(112) of JETSET 7.3 and is as follows:

MST111 =     Order of alpha_s evaluation in ULALPS:
             = 0: fixed alpha_s at the value of PAR111.
             = 1: first-order running alpha_s.
             = 2: second-order running alpha_s.
             (Default = 1).

MST115 =     Treatment of alpha_s singularity at Q2 -> 0:
             = 0: allow it to diverge like 1/ ln(Q2/Lambda^2).
             = 1: soften the divergence to 1/ ln(1 + Q2/Lambda^2).
             = 2: freeze Q2 evolution below Q02 = 4 GeV^2.
             (Default = 0).

PAR111 =     The fixed value of alpha_s assumed in ULALPS when
             MST111 = 0.
             (Default = 0.20).

PAR112 = :   Lambda used in running alpha_s in ULALPS.
             (Default = 0.25).

In the original version of ULALPS, there were additional parameters.
In the modified version included in HERACLES, these have been fixed to
the following values:
             MSTU(112) = 5   (nominal number of flavors used in the
                              expression for alpha_s)
             MSTU(113) = 3   (minimum number of flavors in alpha_s)
             MSTU(114) = 5   (maximal number of flavors in alpha_s)
             PARU(113) = 1.0 (flavor threshold in alpha_s. The quark
                              masses are fixed to 0.3,0.3,0.5,1.5,4.5
                              and 140 GeV for up, down, strange, charm,
                              bottom and top, resp.)
             PARU(114) = 4.0  (Q2 value below which alpha_s is assumed
                              to be constant for MST115 = 2)
             PARU(115) = 10.0 (maximal value of alpha_s returned from
                              ULALPS).


DJANGO FOR HERACLES 4.4
-----------------------

Note that the event simulation of the hadronic final state with routines
from LEPTO and JETSET requires a separation of the total cross section 
into partial cross sections for each flavor of the incoming quark. 
This can be obtained only if parton distribution functions are used. 
The options with ILQMOD = 2 to 5 do not provide parton distributions 
for all x and Q2. They can therefore not be used together with DJANGO6.

The routine PYSSPA, which in former versions had been taken over
from LEPTO 5.2 without changes, has now been changed to allow for the
call of the new version of PYSTFU. These calls are enabled for proton
scattering only. PYSSPA is therefore now contained in DJANGO6 and
has been removed from DJGLEPTO.

A new version of DJANGO6 based on LEPTO 6.5 and JETSET 7.4 has been 
released recently (Oct. 11, 1996).



------------------------------------------------------------------------

DETAILS OF CHANGES IN THE MAIN PROGRAM
--------------------------------------

All changes are related to the new code words and corresponding input.

1) add the following lines

      COMMON /HSALFS/ PAR111,PAR112,MST111,MST115
      REAL*4          PAR111,PAR112
      INTEGER         MST111,MST115

2) replace the following data statement

      DATA CODE/
     1'TITLE     ','EL-BEAM   ','PR-BEAM   ','KINEM-CUTS','EGAM-MIN  ',
     2'INT-OPT-NC','INT-OPT-CC','INT-POINTS','HYP-CUBES ','GSW-PARAM ',
     3'PARTON-DIS','NFLAVORS  ','SAM-OPT-NC','SAM-OPT-CC','RNDM-SEEDS',
     4'GSW-MASS  ','THMIN-QRAD','FLONG     ','          ','          ',
     5'          ','          ','          ','          ','          ',
     6'          ','          ','          ','          ','          ',
     7'          ','          ','          ','          ','          ',
     8'INT-ONLY  ','TEST-OPT  ','IOUNITS   ','START     ','STOP      '/

   by the following new one

      DATA CODE/
     1'TITLE     ','EL-BEAM   ','PR-BEAM   ','KINEM-CUTS','EGAM-MIN  ',
     2'INT-OPT-NC','INT-OPT-CC','INT-POINTS','HYP-CUBES ','GSW-PARAM ',
     3'STRUCTFUNC','NFLAVORS  ','SAM-OPT-NC','SAM-OPT-CC','RNDM-SEEDS',
     4'GSW-MASS  ','THMIN-QRAD','FLONG     ','ALFAS     ','          ',
     5'          ','          ','          ','          ','          ',
     6'          ','          ','          ','          ','          ',
     7'          ','          ','          ','          ','          ',
     8'INT-ONLY  ','TEST-OPT  ','IOUNITS   ','START     ','STOP      '/

3) remove the statements concerning the old input code word 'PARTON-DIS'
   and replace them by the following for 'STRUCTFUNC'

C
C***********************************************************************
C               CONTROL CARD: CODEWD = STRUCTFUNC
C
C               DEFINES THE PARAMETRIZATION OF PARTON DENSITIES
C               OR STRUCTURE FUNCTIONS
C               APPLIED IN THE ACTUAL CALCULATION
C
C***********************************************************************
 1100 CONTINUE
      READ(LUNIN,*) ISTRFC
      ILQMOD=ISTRFC/100000
      IPDFOP=0
      IF (ILQMOD.EQ.0) IPDFOP=1
      LPAR(6)=ISTRFC
      NPYMOD=MOD(ISTRFC,100000)
      IPART=ISTRFC
      WRITE(LUNOUT,'(5X,A,I7)') ' ISTRFC =',ISTRFC
      GO TO 1

4) insert the following for input after code word 'ALFAS'

 1900 CONTINUE
C
C***********************************************************************
C               CONTROL CARD: CODEWD = ALFAS
C
C    DEFINITION OF ALPHA_S IN THE CALCULATION OF THE LONGITUDINAL
C    STRUCTURE FUNCTION
C
C***********************************************************************
      READ(LUNIN,*) MST111,MST115,PAR111,PAR112
      WRITE(LUNOUT,'(5X,A,I5)') ' MST111 =  ', MST111
      WRITE(LUNOUT,'(5X,A,I5)') ' MST115 =  ', MST115
      WRITE(LUNOUT,'(5X,A,F10.4)') ' PAR111 =  ', PAR111
      WRITE(LUNOUT,'(5X,A,F10.4)') ' PAR112 =  ', PAR112
      GO TO 1

5) some other changes concern comment lines and format statements
   which need not be changed.



CHANGES IN THE BLOCK DATA HSBLKD
--------------------------------

1) insert the following lines:

      COMMON /HSALFS/ PAR111,PAR112,MST111,MST115
      REAL*4          PAR111,PAR112
      INTEGER         MST111,MST115

2) replace the following old data statement

      DATA IPART  / 3/

   by the following new one

      DATA IPART  / 110007/

3) insert the following new data statement

      DATA PAR111 /0.2/, PAR112/0.25/, MST111/1/, MST115/0/


++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++



CHANGES IN VERSION 4.5
----------------------

1.) The low Q2 suppression factor has been moved to PYSTFU.

2.) In HMAINS, after reading ISTRFC (code word STRUCTFUNC):
    replace
      IF (ILQMOD.EQ.0) IPDFOP=1
    by
      IF (ILQMOD.LE.1) IPDFOP=1

3.) In HSPRLG, replace
      IF(POLARI.LT.0D0.OR.POLARI.GT.1D0) POLARI=0D0
    by
      IF(POLARI.LT.-1D0.OR.POLARI.GT.1D0) POLARI=0D0

29.09.93

4.) Low Q2 suppression factor: bug removed.

30.09.93

5.) Format statements at the beginning of the routine HSEVTG have
been changed.

8.12.93

6.) New version of HSCC22, treat negative cross section.

22.12.93

7.) New version of structure function parametrization by Badelek
and Kwiecinski, valid now down to x=1E-5.
Replaced subroutines HSBKIN, HSSTBK, and HSF2BK.
additional changes on 12.01.94

12.01.94

8.) Changes in FLTABL to avoid warnings 'outside grid ...', XMAX and
Q2MIN adjusted for use with radiative channels.

6.06.94

9.) All occurences of the line
        IF (LPAR(3).EQ.0) THEN
in subroutine HSSTR1 (member HSSTRFCT) are replaced by
        IF (LPAR(3).LT.3) THEN

19.07.94

10.) Modifications in subroutine HSCCKL to activate charged current
scattering for initial positrons.



++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++



CHANGES IN VERSION 4.6
----------------------

Dec. 1995 

The program has been extended to include elastic scattering ep -> ep
and the radiative tail from quasi-elastic scattering ep -> ep gamma.
The following routines have been added or modified:

Modified routines:  MAIN;
                    HSPRLG, block data HSBLKD, HSEVTG, HSDTIN, HSDOUT;
                    HSACPT;
                    HSLTS1, HSLTS2;
                    PYSTFU;
                    HSWPDF, HSSTRF, HSSTR1;

New routines:       HSELG1 (F)
                    HSELG2 (F)
                    HSEL22 (F)
                    HSELK1 (F)
                    HSELK2 (F)
                    HSELCO (F)
                    HSSGEL (F)
                    HSXMAX (F)
                    HSNRAT (F)
                    HSINIL (S)
                    HSFIE0 (S)
                    HSFIEL (S)
                    HSDELX (S)
                    D01AJF (S)



17.01.96

Change in FLIPOL to treat the case QR(1) = QR(2). This is the corner
of phase space which is reached when x*S = Q2min = 6.0GeV.


30.01.96

Correct bug in low Q2 parametrization of F2 from ALLM: sign in the
expressions for AP and SP in SIGMAR and value of S12 in SIGMAT.