C   08/10/91 410311655  MEMBER NAME  $$README (WWGAMMA.) M  FVS
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%                                                                      %
%                   MONTE-CARLO EVENT GENERATOR                        %
%                              for                                     %
%               Testing Anomalous WW-Gamma Couplings in                %
%               Radiative Charged Current ep Scattering                %
%                      (DESY-Preprint 91-096)                          %
%           (published in Nuclear Physics B373 (1992) 73)              %
%                                                                      %
%                            Authors:                                  %
%                    T. Helbig, H. Spiesberger                         %
%                                                                      %
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%


This library contains subroutines and a sample main program for the
generation of weighted events of the reaction
                    e + p -> nu + gamma + X.
This generator is designed for studies of anomalous couplings of the
charged W boson. The generator is not a Monte Carlo for radiative
corrections to the charged current deep inelastic lepton nucleon
scattering.

The member DEMO contains a sample main program demonstrating the
initialization of the generator, event generation and estimation of the
total cross section.

The member EVENT contains subroutines and functions used in the
Monte Carlo described in DESY-Preprint 91-096. Some important ones
are described in the following:

SUBROUTINE INIT (KAPPA,LAMBDA)

   Initializes the generator and defines the cuts. The cuts are set to
   the values discussed in the Preprint. If needed they can be changed
   in the subroutine INIT. The naming conventions are:

   RCUT=   Cut in quark-photon separation-variable R
   MPTCUT= missing transverse momentum
   PTKCUT= photon transverse momentum
   PT4CUT= scattered quark transverse momentum
   CKECUT= Cos(angle between photon and electron beam)
   CKPCUT= Cos(angle between photon and proton   beam)
   C4ECUT= Cos(angle between quark and electron beam)
   C4PCUT= Cos(angle between quark and proton   beam)
   CSEP=   Cut in Cos(angle between photon and scattered quark),
           (only used as alternative to RCUT)

SUBROUTINE EVENT(P,W,QF)

   Generates one weighted event. The output P, W and QF has the
   following meaning:

   P = four-vectors of outgoing particles P(1:4,0:3), z-axis in proton
       direction !
   P(1,I) = photon
   P(2,I) = neutrino
   P(3,I) = scattered quark
   P(4,I) = proton remnant
   W = weight of event
   QF = flavor of scattered quark
   T_bar =-6
   C_bar =-4
   U_bar =-2
   D     = 1
   S     = 3
   B     = 5
   All quark masses are neglected.

REAL FUNCTION SIGMA ()

   Gives an estimate of the total cross-section based on the generated
   events. To get a good estimate, much more events than needed should
   be produced.


The library WWG.S contains the additional members RNDM (Random
number generator) and PDVAL (parametrizations of parton distribution
functions from Krzysztof Charchula, see F1PCHA.PDS.S), which are
called by EVENT. The member M2 contains the amplitude squared for the
process, common blocks are stored in separate members and read in with
the help of the %MACRO statement.

The random number generator is not initialized in INIT. This has
to be done in the main program by calling the subroutine RNDMST
(contained in member RNDM) or using RNDMREAD and RNDMWRITE to read
and store random number seeds from and to a file.